## Slide 1: Measurement of isomeric states at the FRS Ion Catcher
Timo Dickel
GSI Darmstadt, JLU Gießen
How to study the properties of exotic nuclei via mass spectrometry
The FRS Ion Catcher @ GSI
  Setup
  Performance
  Results
Outlook
  Experiments in FAIR phase-0
  The next generation stopping cell for the Super-FRS
Notes: Introduction

## Slide 2
How to study the properties of exotic nuclei via mass spectrometry

## Slide 3: Mass and Binding Energy
E = mc2
The mass of an atomic nucleus reflects its binding energy
and hence its stability and structure
Z Protons (Proton number)
N Neutrons (Neutron number)
A = N + Z (Mass number)
B = Binding energy
Nuclear mass: M(N, Z) = Z·mp + N·mn - B(N, Z)/c2
Structure & Dynamics
of Exotic Nuclei
Precision mass measurements  unambigious identification in A and Z
Notes: Masses as a window for the information about the BE of the nucleus.

## Slide 4: Mass Measurement Techniques for Exotic nuclei
Isochronous MS
Schottky MS
~500 MeV/u
tmeas ~ 10 s
m/m = 106
δm/m ~ 210-7
broadband
tmeas ~ 100 s
m/m = 2105
δm/m ~ 10-6
broadband
1 eV – 10 keV
Penning Trap MS (TOF-ICR-MS)
tmeas ~ 1 s
m/m = 106-107
δm/m < 10-7
scanning
Storage Rings
„Standard“ Methods
No Method is highly accurate, sensitive and fast
Notes: For measuring masses with high accuracy we can use three types of devices: storage rings, PT and MR-TOF-MS.

## Slide 5: TOF Mass Spectrometry for diagnosis and separation
Enables high performance
Fast  access to very short-lived ions (T1/2 ~ ms)
Sensitive, broadband, non-scanning  efficient, access to rare ions
H. Wollnik et al., Int. J. Mass Spectrom. Ion Processes 96 (1990) 267
Applications
Diagnostics measurements: monitor production, separation and low-energy
beam preparation of exotic nuclei
Direct mass measurements of exotic nuclei
High-resolution mass separator
C. Scheidenberger et al., Hyperfine Interact. 132 (2001) 531
W.R. Plaß et al., NIM B 266 (2008) 4560
W.R. Plaß et al., Int. J. Mass Spectrom. 394 (2013) 134
To achieve high mass resolving power and accuracy:
Multiple-reflection time-of-flight mass spectrometer (MR-TOF-MS)
...
Notes: What is TOF and MR-TOF MS

## Slide 6: Mass Measurement Techniques
Isochronous MS
Schottky MS
~500 MeV/u
tmeas ~ 10 s
m/m = 106
δm/m ~ 210-7
broadband
tmeas ~ 100 s
m/m = 2105
δm/m ~ 10-6
broadband
1 eV – 10 keV
Penning Trap MS (TOF-ICR-MS)
tmeas ~ 1 s
m/m = 106-107
δm/m < 10-7
scanning
Multiple-Reflection Time-of-Flight MS (MR-TOF-MS)
tmeas ~ 10 ms
m/m >105
δm/m < 10-6
Broadband
1 eV – 10 keV
Storage Rings
Notes: For measuring masses with high accuracy we can use three types of devices: storage rings, PT and MR-TOF-MS.

## Slide 7: MR-TOF-MS in RIB Facilities
TRIUMF
MSU
Berkeley
Texas A&M
Oak Ridge
ANL
Notre Dame
RIBRAS
JYFL
ISOLDE
GANIL
GSI/FAIR
SARAF
iThemba
INFN-LNS
VECC
INFN-LNL
Dubna
ELI-NP
IMP-Lanzhou
HIRA
RISP
RCNP
RIKEN
CIAE
ANU
EURISOL
FSU
ALTO
CARIF
HIAF
MR-TOF-MS (operational)
MR-TOF-MS (planned)
MR-TOF-MS (commissioning)
Notes: MR-TOF-MS around the world.

## Slide 8: MR-TOF-MS in RIB Facilities
TRIUMF
MSU
Berkeley
Texas A&M
Oak Ridge
ANL
Notre Dame
RIBRAS
JYFL
ISOLDE
GANIL
GSI/FAIR
SARAF
iThemba
INFN-LNS
VECC
INFN-LNL
Dubna
ELI-NP
IMP-Lanzhou
HIRA
RISP
RCNP
RIKEN
CIAE
ANU
EURISOL
FSU
ALTO
CARIF
HIAF
MR-TOF-MS (operational)
MR-TOF-MS (planned)
MR-TOF-MS (commissioning)
MR-TOF-MS Isobar separator
for the TITAN facility (TRIUMF)
MR-TOF-MS at FRS Ion Catcher (GSI)
Notes: MR-TOF-MS around the world.

## Slide 9
FRS Ion catcher @ GSI

## Slide 10
Super-FRS
FRS
The FRS Ion Catcher at GSI/FAIR
7
Notes: 10

## Slide 11
High-precision experiments with in-flight separated exotic nuclei almost at rest
universal and fast production
high selectivity
cooled exotic nuclei
Super-FRS Experiment Collaboration
(Mass Tagging for PID, New Isotope search, Reaction Studies,…)
MATS (Precision Measurements of very short-lived nuclei
using an Advanced Trapping System for highly charged ions)
LaSpec (Laser Spectroscopy)
In-flight
Production
In-flight
Separation
Momentum
Compression
Stopping /
Thermalization
Target
Fragment
Separator
Buncher /
Degrader
Stopping
Cell
Experiments
(Trap, Laser,..)
Primary
Beam
100...1500 MeV/u
~ eV
~ keV
~ MeV/u
Low Energy RIB @ Super-FRS/FRS
@LEB:
@FRS & LEB:
D. Rodriguez, et a., EPJ 183 (2010) 1
J. Äystö et al., NIMB 376 (2016) 111

## Slide 12
Concept: Cryogenic Stopping Cell (CSC)
IGISOL/Stopping cells:
Fast  access to short-lived exotic nuclides (T1/2 ~ ms)
Universal  element-independent
Efficient  highest stopping and extraction efficiency
Cryogenic Operation
Clean  ion beams of high cleanliness
high energy beam
(~Mev/u)
DC Gradient along the cell
DC to Nozzle
Gas
flow
RF repelling force
Low energy beam (~eV)
M. Ranjan et al., Europhys. Lett. 96 (2011) 52001
Purushothaman S. et al, EPL 104 (2013) 42001
high pressure helium
~100mbar
M. Wada NIM B 317 (2013) 450
Notes: 12

## Slide 13: FRS Ion Catcher
W.R. Plaß et al., NIM B 317 (2013) 457
W.R. Plaß et al, Hypefine Interaction acceppted
FRS
Homogenous
Degrader
DC Cage
RF Carpet
Injection
Trap System
TOF
Analyzer
Isochronous
SEM
BNG
Cryogenic Stopping Cell
RFQ Beam Line +
Diagnostics Unit
Multiple-Reflection
Time-of-Flight Mass Spectrometer
Final Focal Plane
CSC
MR-TOF MS
Production Target
1.6 g/cm2 Be
+ 0.2 g/cm2 Nb
238U @
1000 MeV/u
~ eV
~ MeV/u
~ 500 MeV/u
PID
PID
Slits
Degrader
Slits
~ eV
~ keV
~ MeV/u
~ GeV/u
Notes: FRS Ion Catcher Production mechanism, thermalization, extraction and measurement.

## Slide 14: FRS Ion Catcher
MR-TOF-MS
Low energy (~eV) beamline
Cryogenic stopping cell
Standard detectors for PID
DESPEC
M. Ranjan et al., Europhys. Lett. 96 (2011) 52001
S. Purushothaman et al., EPL 104 (2013) 42001
M. Ranjan et al., NIM A 770 (2015) 87
M.P. Reiter et al., NIM B 376 (2016) 240
F. Greiner et al., NIMB in press
W.R. Plaß et al., NIM B 266 (2008) 4560
W.R. Plaß et al., Int. J. Mass Spectrom. 394 (2013) 134
T. Dickel et al., NIM A 777 (2015) 172
S. Purushothaman et al., IJMS 421 (2017) 245
Notes: More pictures, development in time

## Slide 15
Data-Analysis Procedure
S. Ayet et al PRC 99, 064313 (2019)
Data-analysis procedure optimzed for sensitivity and accuracy:
  dedicated fit function
  weighted MLE fitting
  accurate handling of overlapping peaks
S. Purushothaman et al, IJMS, 421, 245 (2017)
Notes: U Fission Fragments produced at 1GeV. Thermalized, extracted and measured. Note the gaussian fit for guiding the eye.

## Slide 16
Compilation: Mass Measurement Accuracy
Data evaluation developed for low statistics and overlapping peaks
31 masses of 16 different elements including 6 isomeric states:
    Relative deviations down to 6·10-8
    Excitation energies of isomeric states down to 280 keV
    Mass Accuracy Study
weighted mean:
(4.5  5.3) ·10-8
S. Ayet et al PRC 99, 064313 (2019)
Notes: Compilation of the masses evaluated with the current Hyper EMG functions.

## Slide 17: Mass measurement and separation of isomers
MR-TOF-MS enables efficient search and measurement of new isotopes and isomers
m/m = 250,000
TOF = 8.7 ms
1472 keV
Measurement using
the TOF detector
T. Dickel et al., Phys. Lett. B 744 (2015) 137
11
Measurement of excitation energy: (1472  120) keV Literature value: (1462  5) keV

## Slide 18: Mass measurement and separation of isomers
First spatial separation of ground state and isomeric state in an MR-TOF-MS
Proof-of-principle: production of isomerically clean beams by MR-TOF-MS
Separation using the
Bradbury-Nielsen gate,
measurement using
the Si detector
BNG off
BNG on
12
T. Dickel et al., Phys. Lett. B 744 (2015) 137

## Slide 19
Novel method for t1/2 and branching ratios measurements

## Slide 20: Novel method for t1/2 and Branching Ratios
After containment of ~ 2t1/2
Precursor
Recoil 1
Recoil 2
0
31
I. Miskun et al., submitted to EPJA (arXiv:1902.11195)

## Slide 21: Novel method for t1/2 and Branching Ratios
32
Best fitting instrumentation for the task
MR-TOF-MS
broadband and non-scanning
all recoils are measured at the same time
sensitive
precise determination of abundances
accurate
identification and mass measurement
Cryogenic Stopping Cell
clean
no chemical reactions
fast
ions are extracted within few ms
NEW: CSC as an ion trap
all recoils are stopped in buffer gas
Precursor
Recoil 1
Recoil 2
Recoil 3
I. Miskun et al., submitted to EPJA (arXiv:1902.11195)

## Slide 22: Novel method for t1/2 and Branching Ratios
Measured branching ratios
I. Miskun et al., submitted to EPJA (arXiv:1902.11195)
Measured value | Literature value
776 ± 181 ms | 850 ± 90 ms
Energetically possible decays
Internal Transition | β- | β+
1 | 0 | 0
Half-life

## Slide 23: Excitation Energy of 119m2Sb
Ground and isomeric state mass/energy measured directly for the first time
FRS Ion Catcher: (2799 ± 30) keV Lit. (ENSDF): (2841.7 ± 0.4 + x) keV
 x is consistent with 0, and the 2841.7 keV level is the long-lived isomeric state itself
I. Miskun et al., submitted to EPJ A, arXiv:1902.11195v1
2799(30) keV
R.E. Shroy, et al., PRC 19, 1324 (1979)
S. Lunardi, et al., Z. Physik A328, 487 (1987)
M.G. Porquet, et al., EPJ A24, 39 (2005)
C.B. Moon, J. Korean Phy. Soc. 569, 1539 (2011)
2842

## Slide 24
MR-TOF-MS for New Isomers search

## Slide 25
Why a new Method to Measure Isomers?
γγ coincidence
MS (SMS, TOF-ICR)
Requirements for system for isomere search:
  Fast: ~ms
  Sensitive: Non-Scaning
  High Mass Resolving Power: >>105
  High Dynamic Range: > 10:1
Nubase 2012

## Slide 26
Isomer Measurement with MR-TOF-MS
γγ coincidence
MS (SMS, TOF-ICR)
MS and isomeric
beams with MR-TOF
x20
m/Δm(FWHM)~450.000
600MeV/u 124Xe on a 1.6g/cm² Be target
109gIn (9/2+)
109m1In (1/2-)
109m2In (19/2+)
650 keV
2100 keV
109gIn
109m1In
109m2In
t1/2: 209ms
Preliminary

## Slide 27: 124Xe Projectile Fragments: New Isomer Discovered
  Region below 100Sn
  101In
Preliminary
new isomeric state
(9 counts)
new
mass
101gIn+
101mIn+
606(52) keV
FWHM: 230 keV
Due to the high sensitivity and
non-scanning measurement technique, the MR-TOF-MS
is an ideal device for the search
for new isomers
101mIn:
Rate ~2 per hour
Cross-Section ~20 nbarn

## Slide 28
Outlook

## Slide 29
Beta-delayed Neutron Emission
(S472 I. Mardor)
New isotopes search
(S464 S. Pietri)
N=Z isotopes below 100Sn
(S474 W. Plaß)
Approved Beam Times for FAIR Phase-0
38
Multi-Nucleon Transfer Reactions
(S475 T. Dickel)

## Slide 30: New Isotope Search
Identification of new neutron rich isotopes
Measurement of production cross sections and momentum distribution
Mass, half-life and decay spectroscopy measurement after implantation
47 new half lives, 26 new masses and 34 new isotopes
S. Pietri et al.
208Pb fragmentation to produce neutron rich isotopes from Tb to Re
New isotope
New mass
New half-life
Goals:
Mapping frontiers of heavy neutron-rich nuclei
Nuclear structure and shells far-off stability
3d r-process abundance peak

## Slide 31
Outlook – Long Term
From FRS-Ion Catcher Stopping cell ... to ... LEB Stopping Cell
 | Prototype CSC | Super-FRS CSC
Areal density (He) | 6 mg/cm2 | 20…40 mg/cm2
Extraction time | 25 ms | 5…10 ms
Rate capability | 104/s | 107/s
228Th Source
70 K)
incl. finnish in-kind: Helium Recovery Unit
Notes: - Outlook

## Slide 32: Summary and Outlook
Outlook:
  Experiments in FAIR Phase-0
  Next generation CSC for the SuperFRS
The FRS Ion Catcher
  Unique capabilities:
    Efficient thermalization of relativistic secondary beams
    Broadband measurements with full ID
    High mass accuracy, down to 6*10-8
    High sensitivity
    Isomer separation
  Novel method to simultaneous measure mass, Q-value, Branching ratio and half-live
  Search for new isomeric states

## Slide 33
Funding:
BMBF (05P19RGFN1, 05P16RGFN1), State of Hesse (HMWK) (LOEWE Center HICforFAIR), HGS-HIRe, JLU Giessen and GSI (JLU-GSI strategic Helmholtz partnership agreement), European Union Horizon 2020 (654002 JRA SATNURSE), ELI-NP Phase II (1/07.07.2016, CP, ID 1334)
FRS Ion Catcher Collaboration
D. Amanbayev1, S. Ayet1,2, B. Soumya2,9, J. Bergmann1, P. Constantin6, T. Dickel1,2, M. Diwisch1, J. Ebert1, A. Finley7, H. Geissel1,2, F. Greiner1, E. Haettner2, C.Hornung1, S. Kaur8, R. Knöbel2, W.Lippert1, I. Mardor10,11, B. Mei6, I. Miskun1, I. Moore3, J.-H. Otto1, Z. Patyk4, S. Pietri2, A. Pikhtelev8, W.R. Plaß1,2, I. Pohjalainen3, A. Prochazka2, S. Purushothaman2, C. Rappold2, M.P. Reiter1,7, A.-K. Rink1, C. Scheidenberger2, M. Takechi2, Y. Tanaka2, H. Toernquist2, H. Weick2, J.S. Winfield2, X.Xu1,2, M.I. Yavor5
1Justus-Liebig-Universität Gießen, Gießen, Germany;
2 GSI, Darmstadt, Germany;
3 University of Jyväskylä, Jyväskylä, Finland;
4 National Centre for Nucl. Res., Warszawa, Poland
5 Institute for Analytical Instrum., RAS, St. Petersburg, Russia;
6 ELI-NP, Bucharest, Romania;
7 TRIUMF, Vancouver, Canada;
8 Inst. for E. Prob. of Chem. Phys., RAS, Chernogolovka, Russia;
9Saint Mary’s University, Halifax, Canada
10Soreq NRC, Yavne, Israel
11 Tel Aviv University, Tel Aviv, Israel
Acknowledgements
29

## Slide 34
Mass Measurements @ N=126

## Slide 35
Compilation: Mass Measurement Accuracy
    Mass Measuements at N=126
6
First direct measurement
Direct measurement
S. Ayet et al., submitted to PRC, arXiv:1901.11278v1
N=126
Z=82
Notes: Compilation of the masses evaluated with the current Hyper EMG functions.

## Slide 36
Investigation of the N=126 neutron shell, above the Z=82 proton shell
7 ground state masses measured for the first time directly
Short-lived isotopes just above the shell
211Po (512ms), 212At(314ms), 213Rn (19.5ms)
    Mass Measuements at N=126
7
S. Ayet et al., submitted to PRC, arXiv:1901.11278v1
Notes: Compilation of the masses evaluated with the current Hyper EMG functions.

## Slide 37
Investigation of the N=126 neutron shell, above the Z=82 proton shell
Experimental results deviate strongly from the theoretical predictions, especially for N=126 and N=127
    Mass Measuements at N=126
7
S. Ayet et al., submitted to PRC, arXiv:1901.11278v1
A. Sobiczewski and Y. A. Litvinov, PRC 89, 024311 (2014).
W. Myers and W. Swiatecki, NPA 601, 141 (1996).
S. Goriely, N. Chamel, and J. M. Pearson, PRC 88, 024308 2013).
M. Kortelainen et al., PRC 82, 024313 (2010).
Notes: Compilation of the masses evaluated with the current Hyper EMG functions.

## Slide 38: Multiple-Reflection Time-of-Flight Mass Spectrometer
Mass Measurement
Accuracy
Transmission efficiency
Mass
Measurement
2 m
W.R. Plaß et al., NIM B 266 (2008) 4560
W.R. Plaß et al., Int. J. Mass Spectrom. 394 (2013) 134
T. Dickel et al., NIM A 777 (2015) 172
T. Dickel et al., Phys. Lett. B 744 (2015) 137
Kinetic Energy
1.3 keV
Ions
Separated
Ions
Isobar separator with
high ion capacity
Sensitivity
~10-7
up to 70%
World-wide unique combination of
performance characteristics!
~10 ions
>106 ions/s

## Slide 39: Approved Proposal: Detector Test for the LEB & N=Z
Outlook – Short Term
Improvements:
Higher efficiencies
Faster extraction time
Higher mass resolving power
New sources
Cryogenic Stopping Cell
Multiple-Reflection
Time-of-Flight
Mass Spectrometer
Laser Ablation Carbon
Cluster Ion Source
Upgraded Beamline
Notes: Higher Efficiencies:
  Increase areal density
  Optimize transmission
Faster Extraction Times:
  Increase DC Fields
Increase MR-TOF-MS Mass Resolving Power:
  Stabilization power supplies
  Optimization of 25 Hz repetition rate
New Sources:
  Cf for characterization of CSC
  LACCI for isobar calibration

## Slide 40
Motivation for 238U + 164Dy
Rare-earth peak (r-process)
M. Mumpower et al., J. Phys. G, 44 (2017) 3
SA Guiliani et al., https://arxiv.org/abs/1704.00554
M. Eichler at al., Astrophys. J 808 (2015) 30
„East“ of 238U
TLF
PLF
A.V. Karpov, et al PRC 96 (2017) 024618
Proposal: Reaction studies / MNT (S475)
Results for 238U on 164Dy & 64Ni:
    Cross Sections: >150
    New masses: ~20
    Discovery of long-lived isomers G.D. Dracoulis et al.,
      Phys. Scr. T152 (2013) 014015
T. Dickel et al.

## Slide 41
We propose to demonstrate and use a novel method for measuring -delayed single- and multi-neutron emission probabilities (Pxn) (and also mass, Q-values and T1/2), in the following way:
Proposal: beta-delayed neutrons (S472) – Method
I. Mardor et al.

## Slide 42: Mass measurements N=Z below 100Sn
1+
1+
1+
1+
2+
1+
2+
2+
2+
Physics Goals
Resolve inconsistencies in the mass surface (shifts > 1 MeV observed)
Wigner energy, e.g. 80Zr
rp-process: 78Y, 82Nb, 91Rh
New K-Isomers: e.g. 80Zr, 82Zr
High spin isomer in 94Ag (93Pd)
  E. Haettner et al., PRL 106 (2011) 122501
  H. Schatz, W.J. Ong, ApJ 844 (2017) 139
  I Mukha et al., Nature 439 (2006) 298
A. Kankainen et al., PRL 101, (2008) 142503
  AS Lalleman et al., Hyp. Inter. 132 (2001) 315
  Z.J. Bai et al., Chinese Phys. C 40 (2016) 094102
W.R. Plaß et al.
Low yields and short lifetimes
Scarce nuclear physics data
Status and challenges:
Notes: The vicinity of the N=Z line is of special interest in nuclear structure physics, in nuclear astrophysics and for the basic understanding of nuclear forces and symmetries in nuclei.

## Slide 43: CSC: Performance Characteristics
Performance characteristics for 238U projectile fragments produced at 1000 MeV/u
Areal density up to 10 mg/cm² (He)
- five times higher gas density compared to other stopping cells using an RF structure
Ion survival and extraction efficiencies > 60%
- compares favorably to other stopping cells
Total efficiencies up to 30%
- unprecedented for relativistic ions
Extraction times of 25 ms
- access to short-lived nuclei
Rate capability
- full efficiency up to ~104 ions/s
for heavy projectile fragments
S. Purushothaman et al., EPL 104 (2013) 42001
M.P. Reiter et al., NIM B 376 (2016) 240
M.P. Reiter PhD Thesis, JLU Giessen, 2015
> 60%
Notes: First tests with the CSC done. Able to stop and extract relativistic ions.
Areal Density high to achieve maximum of stopping efficiency
Survival efficiency: ion is not neutralized with some molecule
Extraction efficiency: the ions that are stopped and survive, are transported by the RF carpet and extracted

## Slide 44: The Super-FRS CSC
T. Dickel et al., NIMB 376 (2015) 216
Nozzle
@ 70 K
5...10 mbar
@ 70 K
0.01 mbar
@ 300 K
RF carpets
Nozzle
RF
DC
High-
energy ion
beam
Low-energy
ion beam
~
0
.
2
m
Segmented anode
~ 2 m
D
e
t
e
c
t
o
r
10 mbar
-5
@ 300 K
200...300 mbar
High Areal Density Othrogonal extraction – Cryogenic Stopping Cell
HADO-CSC

## Slide 45
T. Dickel et al., NIMB 376 (2015) 216
Nozzle
@70 K
5...10 mbar
@70 K
0.01 mbar
@ 300 K
RF carpets
Nozzle
RF
DC
High-
energy ion
beam
Low-energy
ion beam
~
0
.
2
m
Segmented anode
~ 2 m
D
e
t
e
c
t
o
r
10 mbar
-5
@ 300 K
200...300 mbar
Orthogonal extraction
  short extraction path  faster extraction, higher rate capability
Higher DC field strengths  faster extraction, higher rate capability
Smaller ratio of RF carpet area to stopping volume compared to stopping cells with an RF body  smaller power dissipation
Scales favorably with an increase in length of the stopping volume; (no increase in extra. times, no decrease in extra. efficiencies or rate capability)
Segmented anode  electron current indicates the stopping distribution
Installation of targets in the stopping volume
Ion beam does not hit the RF carpet  no desorption of atoms / molecules
Dual-density design  efficient pumping of the CSC
Advantages of the Novel Design
Higher density
Longer stopping volume
Shorter Extraction path
Higher Field strength