## Slide 1: PANDORA: an experiment to measure nuclear beta decays of astrophysical interest in Magnetized Plasmas
Domenico Santonocito, 26- june-2019, Orsay
Laboratori Nazionali del Sud
Catania
INFN-Pg
INFN-Bo
INFN-LNL

## Slide 2
PANDORA concept
Build a plasma trap where ion species are confined in magnetic field and a plasma is created with:
Electron dens: 1012-1014 cm-3
Electron Temperature: 0.01-100 keV
ion dens. 1011 cm-3
Ion Temperature : ≈ 1 eV
Plasma is well characterized in terms of density, temperature and ion charge states using advanced diagnostics
Investigate possible modifications of b-decaying radio-isotopes lifetimes , a phenomenon predicted by models in strongly ionised atoms !
Variations in lifetimes would have important implications in S and R-processes branching points depend on the “competitive” rates of neutron capture vs. b-decay

## Slide 3
Courtesy of S. Palmerini and M. Busso

## Slide 4: Lifetime variation vs T
Re187(𝛽-)
Courtesy of A. Mengoni
(108 Kelvin)

## Slide 5
A plasma-based facility for interdisciplinary research
PANDORA
Ion Beams Production
In-plasma optical emission measurements of astrophysical interest
Study of nuclear b-decay in plasma

## Slide 6
The B-min configuration suitable for multiply charged ions production
el. dens. 1012-1014 cm-3
el. temperature 0.01-100 keV
Trap Design
The biggest B-minimum Trap ever designed (and hopefully built!) ->This maximizes trapping efficiency
Requirements from physics cases impose operative ECR frequency @ 18 GHz ->This fixes max-B up to 2.4 Tesla
Fix a Maximum B-field (the maximum charge state depends on it)
Coils in SC magnets – exapole in Cu!
Accesses for plasma diagnostics!!
Accesses for decay-product detection!!
PANDORA TRAP DESIGN

## Slide 7
Charge State distribution of the ions in the plasma
It can be modulated by changing the density, the temperature and the “confinement strength” provided by the magnetic field (e thus fixing the ions lifetime)

## Slide 8
PANDORA Conceptual Design

## Slide 9: Multi-diagnostics Setup
SDD: probing volumetric soft X-radiation in the 2 – 20 keV domain
trigger signal
Pinhole camera: providing plasma structural in the range 2 - 20 keV
RF probe + Spectrum analyzer: plasma radio-emission analysis
  Time resolved spectra with 6 ms resolution if triggered by RF probe (useful for instabilities)
VL camera: probing volumetric optical radiation in the 1 – 12 eV domain
HpGe detector
Mass spectrometry: evaluation of CSD
HPGe: providing time integrated X-ray spectra in the 30 - 300 keV domain

## Slide 10
Q.E. ~ 2 ÷ 15 keV
Sensor Size: 26.6 mm x 26.6 mm
(1024 x 1024 Pixels)
Max Energy Resolution ~ 150 eV
Lead Pin-hole (diameters 400 μm)
Space resolved X-ray analysis

## Slide 11
Escape Peak
Dimer Peak
Ar
Ti
Ta
Energy Resolution ~ 230 eV at 8.1 keV (Ta-La fluorescence line)
Space resolved X-ray analysis

## Slide 12
Ar
Ti
Ta
L=10
S=5
Plasma structure inspection
Tantalum
Tantalum
Argon
Titanium
Titanium
Info on:
Plasma density
Intensity of losses in
plasma

## Slide 13: Optical emission spectroscopy at INFN-LNS
H spectrum
2019
2016
Δλ = 2nm
R = 250
H, Ar
CR model
2017
Δλ = 1nm
R = 500
H
CR model
2018
Δλ = 0.04nm
R=12500nm
H, Ar
CR model
YACORA
Collisional Radiative (CR) model is used to evaluate density and temperature from line ratios
In collaboration with Max Plank Institute Institute of Plasma Physics (Germany)
2018
Δλ = 0.17nm
R=3000
H, Ar
CR model
We started to measure in H2 plasmas

## Slide 14: Optical emission spectroscopy at INFN-LNS
2019
Δλ = 0.003nm
R=164000
any
CHIANTI
Astrophysical database to ECR plasmas
In collaboration with
University of Michigan
and Cambridge University
The powerful spectropolarimeter SARG (Spettrografo Alta Risoluzione Galileo, moved from TNG – Canary Islands to INFN-LNS), operating at R=164000, will allow in-plasma on-line charge state distribution discrimination.
2016
Δλ = 2nm
R = 250
H, Ar
CR model
2017
Δλ = 1nm
R = 500
H
CR model
2018
Δλ = 0.04nm
R=12500nm
H, Ar
CR model
2018
Δλ = 0.17nm
R=3000
H, Ar
CR model
At higher and higher resolutions, it is possibile to see the shift of emission lines due to multi-ionization

## Slide 15
X-ray burst RF burst: trigger signal
Radial X-ray
Axial X-ray
Axial X-ray
Radial X-ray
RF emission
RF emission
Plasma-self emission:
Sub-harmonics
Main RF frequency
of plasma heating
When modifying the axial magnetic field profile, the X-ray emission “jumps” and becomes pulsed instead of CW
RF burst  trigger signal
Axial and radial X-ray measurements  X-ray burst
Spectrogram  microwave plasma-self emission
TIME-Resolved RF + Soft/Hard X ray Spectroscopy

## Slide 16
The decay-products can be tagged by the emitted γ-rays using an array of GE detectors or scintillators (ex. LaBr3)
Measurement of b-decays in a plasma trap
A “buffer plasma” is created by He, O or Ar up to densities of 1013 cm-3
The isotope is then directly fluxed (if gaseuous) or vaporized inside the chamber
Relative abundances of buffer vs. isotope densities range from 100:1 (if the isotope is in metal state) to 3:1 (in case of gaseous elements
  For PANDORA’s trap, expected up to 1 MeV (<1 counts/sec)
Plasma self-emission must be taken into account
Simulations of efficiencies, signal/noise ratio

## Slide 17
Number of decays
Isotope activity
Density of the isotope in the plasma (const.)
Plasma volume (const.)
As a consequence of dynamical equilibrium
Total decays depend linearly on meas. Time !!
Monitoring of plasma density, temperature and CSD becomes crucial!!
Measurement of b-decays in a plasma trap

## Slide 18
In-plasma isotope concentration = 1011 cm-3
Plasma volume=1000 cm3
Scientific cases under investigations
134Cs
94Nb
Assuming dynamical equilibrium, the total number of g emitted over the entire solid angle can be estimated
Geant-4 simulations have been carried our right for determining geometrical and photo-peak efficiency, including branching of g-lines for each of the selected physics cases
Measurement of half-lives of radioactive nuclei sited at possible branching ratios along the n-capture path
Feasibility -> tagging using gamma-ray emission
-> lifetime in a measurable range
-> easy access to the samples
134Cs 2.06 > 600
94Nb 2.03x104 > 700
81Kr 2.29x105 276
176Lu 3.78x1010 88-400
t1/2 (yr) Eg(KeV)
187Re 176Lu

## Slide 19
176Lu - cosmochronometer
Lifetime variation vs Temperature
176Lu T1/2 = 3.78 x 1010 yr
Calculation by A. Mengoni
Ne =1026
Ne = 1018

## Slide 20
176Lu - cosmochronometer
10 20 40 60 80 days
100
80
60
40
20
10
1
Effective activity in plasma (cps)
2 106
107
Lifetime [years]
8 105
4.0 105
2.6 105
2.0 105
1.6 105
176Lu T1/2= 3.78 x 1010

## Slide 21
134Cs (b-)  134Ba
T1/2 = 2.06 yr
134Cs nucleus
Lifetime variation vs Temperature
Calculation by A. Mengoni

## Slide 22
Chart: 
 | 810 | 1120 | 145 | 150 | 100
Item | Cost [k€] | Description | 
Coil 1 | 150 | SC technology | 
Coil 2 | 150 | SC technology | 
Coil 3 | 150 | SC technology | 
Lhe Cryostats (3) | 60 | SC coils cooling | 
Iron | 50 | monocoil hexapole technology | 
Hexapole in Copper | 250 | monocoil hexapole technology | 
SUBTOTAL | 810 |  | 
Germanium Detectors | 1120 | 14 HpGe detectors including cooling and electronics | 
SUBTOTAL | 1120 |  | 
Vaporization system | 30 | high-temp. Oven | 
Sputtering system | 15 | movable sputtering system | 
Isotopes procurement | 100 | Rare isotopes purchase | 
SUBTOTAL | 145 |  | 
Pumping | 50 | vacuum system | 
Controls | 50 | remote control of the Trap | 
Ancillaries&Cons. | 50 | microwave connections, mechanics etc. | 
SUBTOTAL | 150 |  | 
Plasma Diagnostics Upgrade | 100 | Construction | 
SUBTOTAL | 100 |  | 
TOTAL | 2325 |  | 
Cost estimations of the PANDORA setup
Total: 2.3 - 2.5 MEuro

## Slide 23
Conclusions
New approach to Astrophysics and Nuclear Astrophysics using a plasma trap to investigate possible modifications of b-decaying radio-isotopes lifetimes
Developed complex diagnostic systems to extract plasma parameters (density, Temperature, charge states)
Experimental setup based on Ge detectors to tag the gamma decay following beta emission
Selected few physics case as test case to investigate the quality of this new approach.

## Slide 25
Injection of rare isotopes in the magnetoplasma
Short lifetime
(e.g. 7Be, 13N, 15O)
Charge Breeding
(in-flight-in-plasma capture)
Long lifetime
(e.g. 176Lu, 81Kr)
Classical evaporation systems
(resistive/inductive ovens)
This is more feasible as a first step!!

## Slide 26
plasma
80 cm
35 cm
The biggest B-minimum Trap never designed (and hopefully built!);
  This maximizes trapping efficiency
Requirements from physics cases impose operative ECR frequency @ 18 GHz
  This fixes max-B up to 2.4 Tesla
To maximize space availability for diagnostics and γ-detection, we opted for HYBRID solution
   Coils NbTi, mono-coil-hexapole in Copper… BUT… we need feedbacks from manufacturers
PANDORA TRAP DESIGN